# Access Control System User’s Manual

# Please read this manual thoroughly before installation.

# 1. Brief Product Introduction:

This access control system, which is currently one of the advanced  access systems. It uses the latest central process unit (CPU) and memory chip of large capacity. There will be of no information loss even in case of power failure. It takes the latest HOMMARD technology,

The perfect security functions let the users feel much more safe, which include door state monitoring, alarm output, safety mode, anti dismantling, RFID card and password. While its functions of opening button, close notification, door bell, to be connected with NO. and NC. locks bring more operating easiness to the users.

This product provides access control mode, which is safe and fully automatic, it is an ideal device for business organizations, offices, factories, residences and communities.

2. Technical Features

| No. | Item | Specification |
| --- | --- | --- |
| 1 | Power supply | DC: Voltage 12V±10%; current < 0.1A |
| 2 | Max load | Alarm output: 100mA Electrolock output: 5A |
| 3 | Dimension | 116mm×116mm×20mm |
| 4 | Weight | 160g |
| 5 | Ambient temp. | -20℃—60℃ |
| 6 | RH | 20%—90% |

# 3、Status Indications:

# LED Indicators

| Status | Red LED | Green LED |
| --- | --- | --- |
| Normal state | Flash |  |
| Open |  | Light |
| Key Press | Light |  |
| Program Mode | Light | Flash frequent |
| Set OK | Light | Light |
| Alarm | Flash |  |

Buzzer

| Status | Description | Buzz |
| --- | --- | --- |
| Key Press | Short beep once | Bi |
| Input valid password | Two short beeps | BiBi |
| Input wrong password | Long beep once | Bi—— |
| Alarm state | Continuous long beeps | Bi—Bi—Bi— |

# 4. Setup:

- Default value: Login password  9 9 9 9  ,User password   1 2 3 4

- Enter programming mode:

Press  *    Login password    #  enter programming mode.

- Function setup (should be in programming mode):

1). Modify login password.

Press   0     new password    #    confirm new password    #

Note: the new password should be any 1-8 figures.

2).Modify user password.

Press   1     new password    #    confirm new password    #

Note: the new password should be any 1-8 figures.

3).Set the length of open time:

Press  2     X   X    # .

Note: XX is from 00-99, unit is second, factory setting is 6 seconds.

4).Set the length of alarm time:

Press  3     X   X    # .

Note: XX is from 00-99, unit is minute, factory setting is 5 minutes.

5).Set door state monitoring mode:

Press  4     0   0    #  to disable this function.

Press  4     0   1    #  to enable this function.

Note: to enable door state monitoring, reed switches must be installed, when this function is enabled, the following two functions can also be enabled at the same time:

- If the user put in the correct password to open the door, then forget to close the door, the buzzer will give audible sound to note the user.

- If the door is opened illegally, the system will activate alarm signal output, at the same time, buzzer emits sound alarm.

6). Set safety mode:

Press  5    0   0    #  to disable this function.

Press  5    0   1    #  to read 10 invalid cards or valid cards, then enter 4 wrong passwords successively, the system is locked for 10 minutes.

Press   5    0   2    #  to read 10 invalid cards or valid cards, then enter 4 wrong passwords successively, the system activates alarm signal output.

Note: factory setting this function is disabled.

7) Save the settings and exit programming mode:

Press  *  .

Note: * should be pressed within 1 minute to save the setting when any of the above operation is completed.

4.     How to use:

1). In normal work mode, can be open by user password.

2). If input the mistake, connect to double-click *

3). If program password is forgotten, you can use jumper switch“RESET”at the main board to restore factory setting. First, power off. Then set jumper switch to“ON”position. Power on. Shift the jumper switch back to “OFF”position after three beeps of the buzzer, now the factory setting is restored.

Attachment: wiring diagram for installation

NOTE: 1. Power off before installation wiring,

hot line work is forbidden!!

2. Normally, electrolock is connected out

from power controller.